| Title | Assemble and service moulds, and demould products for precast concrete product manufacture |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | People credited with this unit standard are able to: prepare to assemble, and assemble moulds for precast concrete product manufacture; prepare to demould, and demould precast concrete products; service moulds for precast concrete product manufacture; and complete work operations. |
| --- | --- |

| Classification | Concrete > Precast Concrete |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refer to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Workplace practice refers to the documented procedures specific to a workplace which set out the standard and required practices of that workplace.

2	For the purpose of this unit standard, moulds can be one-sided.

3	Assessment against this unit standard must be undertaken on site.  On site refers to a wide range of building and construction environments within which trade skills are required, and includes concrete production and concrete construction sites.

4	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the uniformity, finish quality, and material economies currently accepted within industry.

5	Legislation relevant to this unit standard includes:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

NZS 3109:1997 Concrete construction and NZS 3114:1987 Specification for concrete surface finishes, available from Standards New Zealand (http://www.standards.co.nz).

Outcomes and performance criteria

Outcome 1

Prepare to assemble moulds for precast concrete product manufacture.

Performance criteria

1.1	Requirements for moulds are determined in accordance with job specifications, NZS 3109, and NZS 3114.

Range	dimensional tolerances, finish requirements, sealing, release tapers, concrete pressures, grout losses, form removal, access, plant.

1.2	Mould components are checked against job specifications and any identified faulty components are replaced.

1.3	Tools, equipment, and personal protective equipment are identified and selected in accordance with job requirements and workplace practice.

Outcome 2

Assemble moulds for precast concrete product manufacture.

Performance criteria

2.1	Mould assembly sequence is in accordance with workplace practice and job requirements.

2.2	Fittings, fixings, and hardware are attached in accordance with job specifications and workplace practice.

2.3	Tolerances are in accordance with job specifications and workplace practice.

2.4	Mould surface is treated in accordance with job specifications and manufacturer’s specifications.

Range	treatment materials – one of: release agents, oil, retarder.

2.5	Assembled mould meets pre-pour checks against workplace quality control requirements.

Outcome 3

Prepare to demould precast concrete products.

Performance criteria

3.1	Requirements for demoulding product are determined in accordance with job specifications.

Range	demoulding sequence, access, plant.

3.2	Tools, equipment, and personal protective equipment are identified and selected in accordance with job requirements and workplace practice.

Outcome 4

Demould precast concrete products.

Performance criteria

4.1	Demoulding sequence is performed in accordance with workplace practice.

4.2	Product is removed from mould and prepared for storage without damage to product or mould.

Range	factors to consider – frames, lifting and handling process, cranage, impact of forces, suction pressure, concrete strength, labelling.

4.3	Mould is cleaned and prepared for reuse or storage in accordance with workplace practice.

Outcome 5

Service moulds for precast concrete product manufacture.

Performance criteria

5.1	Mould is inspected and overall condition assessed, and requirements for servicing are identified in accordance with workplace practice.

5.2	Mould is serviced to meet manufacturer’s specifications and in accordance with workplace practice.

Range	cleaning, repair or replacement of parts, corrosion protection.

Outcome 6

Complete work operations.

Performance criteria

6.1	All operations are safely completed, workplace and equipment are cleaned in accordance with workplace practice and environmental safety requirements, and routine maintenance is carried out in accordance with workplace practice.

| Replacement information | This unit standard replaced unit standard 12028. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 20 November 2009 | 31 December 2024 |
| Review | 2 | 24 November 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.