| Title | Install and service pneumatic or electro-pneumatic equipment |
| --- | --- |
| Level | 3 | Credits | 5 |

| Purpose | People credited with this unit standard are able to: – install pneumatic or electro-pneumatic equipment; – test pneumatic or electro-pneumatic equipment; and – service pneumatic or electro-pneumatic equipment. |
| --- | --- |

| Classification | Industrial Measurement and Control > Industrial Measurement and Control - Maintenance |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	This unit standard has been developed for learning and assessment in a workplace environment.

2	References

ANSI/ISA-51.1-1979 (R1993) Process Instrumentation Terminology;

Electricity Act 1992;

Electricity (Safety) Regulations 2010;

Health and Safety at Work Act 2015 and associated regulations;

ISSN 0114-0663, New Zealand Electrical Codes of Practice, available from Worksafe, https://worksafe.govt.nz/;

and all subsequent amendments and replacements.

3	Definitions

Industry requirements – includes all asset owner requirements; manufacturers’ specifications; enterprise requirements which cover the documented workplace policies, procedures, specifications, and business requirements; and quality management requirements relevant to the workplace in which the assessment is carried out.

Service – planned activity during normal operation, that involves, inspection, cleaning, testing, adjusting or making minor repairs to a piece of equipment to ensure that it works properly.

4	Range

Pneumatic or electro-pneumatic equipment – cylinders, control valves, pressure relief valves, pressure regulators, driers, boosters;

evidence of at least one type of equipment is required.

5	Recommended skills and knowledge: Unit 28083, Demonstrate knowledge of hydraulic and pneumatic control equipment used in industrial process control applications; and Unit 2630, Demonstrate knowledge of pressure measurement systems used in industry.

Outcomes and performance criteria

Outcome 1

Install pneumatic or electro-pneumatic equipment.

Performance criteria

1.1	Select devices according to process conditions and accuracy requirements of the installation.

Range	may include but is not limited to – pressure, flow, temperature, materials.

1.2	Install devices using selected materials.

Range	may include but is not limited to – tubing, piping, threading, mounting, sealants, isolation.

1.3	Commission pneumatic or electro-pneumatic equipment.

Range	may include but is not limited to – bleeding system, leak testing.

Outcome 2

Test pneumatic or electro-pneumatic equipment.

Performance criteria

2.1	Explain and follow safe work procedures.

Range	may include but is not limited to – process isolation, loop isolation.

2.2	Select test equipment according to accuracy and range of devices.

Range	may include but is not limited to – gauges, test set, electrical solenoid supply.

2.3	Identify type and cause of typical errors.

Range	may include but is not limited to – air leaks, solenoid failure.

2.4	Adjust devices, as specified by the data sheet.

2.5	Document test results in accordance with industry requirements.

Outcome 3

Service pneumatic or electro-pneumatic equipment.

Performance criteria

3.1	Locate, interpret, and apply technical information for servicing equipment.

3.2	Explain and follow safe work procedures.

Range	may include but is not limited to – process isolation, loop isolation.

3.3	Complete servicing of equipment to ensure continued operation.

Range	may include but is not limited to – tools, materials, parts, techniques, specifications.

3.4	Produce reports and documentation in accordance with industry requirements.

| Planned review date | 31 December 2021 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 31 October 1995 | 31 December 2013 |
| Revision | 2 | 30 October 1997 | 31 December 2013 |
| Revision | 3 | 3 April 2001 | 31 December 2013 |
| Review | 4 | 22 June 2001 | 31 December 2013 |
| Review | 5 | 19 May 2008 | 31 December 2019 |
| Review | 6 | 21 November 2013 | N/A |
| Rollover and Revision | 7 | 28 June 2018 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.