| Title | Describe and operate primary and secondary preparation equipment on electricity structures |
| --- | --- |
| Level | 4 | Credits | 12 |

| Purpose | People credited with this unit standard are able to: describe health and safety requirements for carrying out primary and secondary preparation; describe primary and secondary preparation equipment; and operate primary and secondary preparation equipment, on electricity structures. |
| --- | --- |

| Classification | Electricity Supply > Electricity Supply - Transmission Networks |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Evidence presented for assessment against this unit standard must be consistent with safe working practices and be in accordance with applicable legislative and industry requirements.

2	Legislation, regulations, and /or industry standards relevant to this unit standard include but are not limited to:

- Electricity Act 1992

- Health and Safety at Work Act 2015

- Health and Safety at Work (General Risk and Workplace Management) Regulations 2016

- Electricity supply industry codes of practice and documented enterprise procedures, including Safety Manual – Electricity Industry (SM-EI) and relevant EEA guides available at www.eea.co.nz

and any subsequent amendments and replacements.

3	Definitions

Asset owner refers to a participant who owns or operates assets used for generating or conveying electricity.

Industry requirements include all asset owner requirements; manufacturers’ specifications; and enterprise requirements which cover the documented workplace policies, procedures, specifications, and business and quality management requirements relevant to the workplace in which assessment is carried out.

Primary preparation is defined as pressure washing, water cleaning performed at less than 34MPa.

Secondary preparation is defined as the removal of rust and zinc corrosion products (ZCP) from electricity structures.

4	Assessment of practical skills against the outcomes in this standard requires three practical observations from three different workplace activities in an electricity supply environment.

Outcomes and performance criteria

Outcome 1

Describe health and safety requirements for carrying out primary and secondary preparation on electricity structures.

Performance criteria

1.1	Health and safety requirements are explained for primary and secondary preparations.

1.2	Restrictions on abrasive blasting media used in the workplace are described in accordance with the Health and Safety at Work (General Risk and Workplace Management) Regulations 2016.

1.3	Potential workplace hazards using primary and secondary preparation equipment are described in accordance with company and industry requirements.

1.4	Health hazards of primary and secondary preparation operations are described in terms of short and long term physical effects.

1.5	Requirements for the provision and maintenance of protective clothing	are described.

Outcome 2

Describe primary and secondary preparation equipment on electricity structures.

Performance criteria

2.1	Primary and secondary preparation equipment is described in terms of its classification.

2.2	Components of primary and secondary preparation equipment are identified and functions are described.

2.3	Safety precautions in the operation of primary and secondary preparation equipment are described.

2.4	Methods of defining secondary preparation areas are described in accordance with company and industry requirements.

2.5	Pre-operational checks are described.

Outcome 3

Operate primary and secondary preparation equipment on electricity structures.

Performance criteria

3.1	Pre-operational checks are made prior to commencement of work.

3.2	Personal protective equipment for the job is checked, fitted and worn in accordance with manufacturer’s instructions and company requirements.

3.3	Water purity is tested prior to use.

3.4	Work site is set up ready for primary and secondary preparation operations according to the job specification and industry requirements.

3.5	System is flushed with sufficient water to clean equipment prior to use.

3.6	Primary preparation operations are applied to electricity structures according to the job specification.

3.7	Secondary preparation operations are applied to electricity structures according to the job specification.

3.8	Work site is demobilised on completion, and equipment is cleaned and stored in accordance with manufacturer’s instructions and company procedures.

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 20 August 2015 | 31 December 2020 |
| Review | 2 | 28 September 2017 | N/A |
| Rollover and Revision | 3 | 2 March 2023 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0120 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Waihanga Ara Rau Construction and Infrastructure Workforce Development Council at qualifications@WaihangaAraRau.nz if you wish to suggest changes to the content of this unit standard.