| Title | Make as-built drawings and record variations to job specifications for drainlaying jobs |
| --- | --- |
| Level | 4 | Credits | 5 |

| Purpose | This unit standard is for people who work, or intend to work, in drainlaying. People credited with this unit standard are able to make as-built drawings and record variations to job specifications for drainlaying jobs. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Drainlaying |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Building Act 2004;

Health and Safety at Work Act 2015;

and their subsequent amendments and replacements.

2	Definitions

Job documentation – drawings and job specifications.

Job requirements –specific requirements of the job at hand not covered by job specifications.

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturer instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

Approving authority – includes but is not limited to territorial authorities, network utility operators, and building consent authorities.

3	Drawings may be plans as relevant to the drainlaying sector.  It is not expected that instruments will be used for drawing.  Drawings are to suit the purpose of worksite communication.

4	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

Outcomes and performance criteria

Outcome 1

Make as-built drawings and record variations to job specifications for drainlaying jobs.

Performance criteria

1.1	Make as-built drawings in sufficient detail to determine if the requested work is compliant and if alterations are required during the work.

1.2	Make as-built drawings in sufficient detail to allow needed material, time, and equipment to be determined.

1.3	Make as-built drawings in sufficient detail to enable the designer to create a plan for approval or amend the original plan and submit it to the approving authority for approval.

| Replacement information | This unit standard, unit standard 30526, unit standard 30527, and unit standard 30528 replaced unit standard 21879 and unit standard 21882. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 28 September 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.