| Title | Install inspection chambers |
| --- | --- |
| Level | 3 | Credits | 2 |

| Purpose | This unit standard is for people who work in the drainlaying industry. People credited with this unit standard are able to install inspection chambers. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Drainlaying |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Plumbers, Gasfitters, and Drainlayers Act 2006;

Health and Safety at Work Act 2015;

Building Act 2004;

Health Act 1956;

Resource Management Act 1991;

Plumbers, Gasfitters, and Drainlayers Regulations 2010;

The following standards, which are available at http://www.standards.govt.nz:

AS/NZS 1547:2000 On-site domestic wastewater management

AS/NZS 1546.1:2008 On-site domestic wastewater treatment units – Septic tanks

AS/NZS 3500.2:2003 Plumbing and drainage – Sanitary plumbing and drainage;

The following guides, which are available at http://www.worksafe.govt.nz/worksafe:

Good practice guidelines – Excavation safety, Wellington: WorkSafe New Zealand, 2016

Guide for Safety with Underground Services, Wellington: Department of Labour, 2002;

The following clauses, and any related compliance documents, which are available at https://www.building.govt.nz/:

New Zealand Building Code Clause E1 Surface Water

New Zealand Building Code Clause G12 Water Supplies

New Zealand Building Code Clause G13 Foul Water;

and all subsequent amendments and replacements.

2	Definitions

Inspection chamber – a chamber with working space at ground level through which the drain passes either as an open channel or as a pipe incorporating an inspection point.

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturers’ instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

Other services – any existing installed services such as water, gas, electricity, or telephone network cables.

3	All practical activities are to be carried out in a way that avoids harm to people and damage to property, environment, other services, materials, tools, and equipment.

4	Any preparatory and finishing work associated with the installation of inspection chambers must be carried out in accordance with the requirements of the job specifications, site conditions, relevant standards and codes, and the Building Act 2004.  This may include but is not limited to excavation, base stabilisation, backfill and compaction, site remediation.

5	Range

Inspection chambers are limited to wet chambers and may include but are not limited to – pre-cast concrete, in-situ, plastic, in-line inspection chambers, drop inspection chambers.

6	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

7	Recommended skills and knowledge for the unit standard: Unit 30532, Demonstrate knowledge of excavating and trenching for plumbing, gasfitting, or drainlaying, and Unit 30533, Position, excavate, and backfill excavations and trenches for plumbing, gasfitting, or drainlaying.

Outcomes and performance criteria

Outcome 1

Install inspection chambers.

Performance criteria

1.1	Select appropriate inspection chambers.

1.2	Position inspection chambers appropriately.

1.3	Install channel, invert level between inlet and outlet, benching, and risers.

1.4	Use appropriate methods of jointing pipework to inspection chambers according to the materials being joined.

Range	loose sleeve/band clamped sleeve, plaster/epoxy mortar (epoxy resin), rubber ring;

evidence of two is required.

1.5	Install lid and adjustment rings.

| Replacement information | This unit standard and unit standard 30534 replaced unit standard 1116. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 28 September 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.