| Title | Demonstrate knowledge of pumps used in drainlaying systems |
| --- | --- |
| Level | 4 | Credits | 3 |

| Purpose | This unit standard is for people who work in the drainlaying industry. People credited with this unit standard are able to demonstrate knowledge of: – pumps used in drainlaying; – selecting pumps, filters, and controls for drainlaying systems; – concepts and principles underpinning the installation of pump stations; and – maintenance of pumps used in drainlaying systems. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Drainlaying |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Building Act 2004;

Health Act 1956;

Health and Safety at Work Act 2015;

Plumbers, Gasfitters, and Drainlayers Act 2006;

Plumbers, Gasfitters, and Drainlayers Regulations 2010;

Resource Management Act 1991;

The following standards, which are available at http://www.standards.govt.nz:

AS/NZS 1546.1:2008 On-site domestic wastewater treatment units – Septic tanks, AS/NZS 1547:2012 On-site domestic wastewater management,

AS/NZS 3500.2:2015 Plumbing and drainage – Sanitary plumbing and drainage;

The following guides, which are available at http://www.worksafe.govt.nz;

Excavation Safety – Good practice Guidelines,

Underground services – Guide for safety with underground services;

The following clauses, and any related compliance documents, which are available at https://www.building.govt.nz/:

New Zealand Building Code Clause E1 Surface Water,

New Zealand Building Code Clause G12 Water Supplies,

New Zealand Building Code Clause G13 Foul Water;

and all subsequent amendments and replacements.

2	Credit for this unit standard does not entitle the candidate to legally perform certain electrical aspects of this work unless registered or supervised by a registered person under the provisions of the Electricity Act 1992.

3	Definition

Drainlaying systems – drainage systems for the disposal of foulwater or stormwater that are constructed to convey the collected water to an appropriate outfall, using gravity flow where possible, but other means when necessary.

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturer instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

4	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

5	Recommended skills and knowledge for the unit standard: Unit 30532, Demonstrate knowledge of excavating and trenching for plumbing, gasfitting, or drainlaying.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of pumps used in drainlaying.

Performance criteria

1.1	Describe the types of pumps that are available and appropriate for use in drainlaying applications.

1.2	Determine pumping requirements to meet job specifications.

Outcome 2

Demonstrate knowledge of selecting pumps, filters, and controls for drainlaying systems.

Performance criteria

2.1	Describe factors that impact the selection of pumps, filters, and controls for drainlaying systems in accordance with job specifications.

Range	suction lift, viscosity, water type, delivery head, required flow rate, frictional head loss, size requirements.

2.2	Explain alarm and monitoring systems and pump switch operations for pump installations.

2.3	Explain testing and commissioning processes for pumps used in drainlaying systems.

2.4	Identify what information is needed to determine the appropriate pump for a given application.

2.5	From pump specifications, determine whether a pump is appropriate (or not) for a given application.

Outcome 3

Demonstrate knowledge of concepts and principles underpinning the installation of pump stations.

Range	pump stations include sewerage, storm water, trade waste.

Performance criteria

3.1	Explain underpinning concepts and principles in terms of their application to the installation of pumps in drainlaying systems.

Range	corrosion, head, hydrostatics and hydraulics, pressure.

3.2	Describe processes for jointing methods appropriate for the materials being joined.

Range	loose sleeve/band clamped sleeve, flange, glue/solvent cement/solvent weld, screwed thread, fusion welding.

Outcome 4

Demonstrate knowledge of maintenance of pumps used in drainlaying systems.

Performance criteria

4.1	Describe preventative and ongoing maintenance requirements and processes for pumps.

4.2	Describe how to identify faults in terms of causes and means of rectification.

4.3	Describe how to rectify faults in accordance with maintenance requirements and job specifications.

| Replacement information | This unit standard and unit standard 30601 replaced unit standard 1118. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 26 October 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.