| Title | Install pumps for drainlaying systems |
| --- | --- |
| Level | 4 | Credits | 2 |

| Purpose | This unit standard is for people who work in the drainlaying industry. People credited with this unit standard are able to install pumps for drainlaying systems. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Drainlaying |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Building Act 2004;

Health Act 1956;

Health and Safety at Work Act 2015;

Plumbers, Gasfitters, and Drainlayers Act 2006;

Plumbers, Gasfitters, and Drainlayers Regulations 2010;

Resource Management Act 1991;

The following standards, which are available at https://www.standards.govt.nz/;

AS/NZS 1546.1:2008 On-site domestic wastewater treatment units – Septic tanks, AS/NZS 1547:2012 On-site domestic wastewater management,

AS/NZS 3500.2:2015 Plumbing and drainage – Sanitary plumbing and drainage;

The following guides, which are available at http://www.worksafe.govt.nz;

Excavation Safety – Good practice Guidelines,

Underground services – Guide for safety with underground services;

The following clauses, and any related compliance documents, which are available at https://www.building.govt.nz/:

New Zealand Building Code Clause E1 Surface Water,

New Zealand Building Code Clause G12 Water Supplies,

New Zealand Building Code Clause G13 Foul Water;

and all subsequent amendments and replacements.

2	Credit for this unit standard does not entitle the candidate to legally perform certain electrical aspects of this work unless registered or supervised by a registered person under the provisions of the Electricity Act 1992.

3	Definitions

Drainlaying systems – drainage systems for the disposal of foulwater or stormwater that are constructed to convey the collected water to an appropriate outfall, using gravity flow where possible, but other means when necessary.

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturer instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

Other services – any existing installed services.

4	Any preparatory and finishing work associated with the installation of pumps and associated equipment must be carried out in accordance with the requirements of the job specifications, site conditions, relevant standards and codes, and the Building Act 2004.  These may include but are not limited to excavation, base stabilisation, backfill and compaction, and site remediation.

5	All practical activities must be carried out in a way that avoids harm to people and damage to property, environment, other services, materials, tools, and equipment.

6	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

7	Recommended skills and knowledge for the unit standard: Unit 30532, Demonstrate knowledge of excavating and trenching for plumbing, gasfitting, or drainlaying.

Outcomes and performance criteria

Outcome 1

Install pumps for drainlaying systems.

Performance criteria

1.1	Position and install pump, and associated fittings, and connect to discharge point.

Range	associated fittings – valves, fittings, discharge pipe.

1.2	Test pump and delivery system for correct operation and soundness of installation.

| Replacement information | This unit standard and unit standard 30600 replaced unit standard 1118. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 26 October 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.