| Title | Demonstrate knowledge of trade waste interceptor traps |
| --- | --- |
| Level | 3 | Credits | 4 |

| Purpose | This unit standard is for people who work in the plumbing or drainlaying industries. People credited with this unit standard are able to demonstrate knowledge of: – trade waste types, sources, and its interception for appropriate management – the installation of trade waste interceptor traps; and – good practice relating to the installation and hand-over of trade waste interceptor traps. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Drainlaying |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Building Act 2004;

Health Act 1956;

Health and Safety at Work Act 2015;

Plumbers, Gasfitters, and Drainlayers Act 2006;

Plumbers, Gasfitters, and Drainlayers Regulations 2010;

Resource Management Act 1991;

The following standards, which are available at http://www.standards.govt.nz:

AS/NZS 1546.1:2008 On-site domestic wastewater treatment units – Septic tanks, AS/NZS 1547:2012 On-site domestic wastewater management,

AS/NZS 3500.2:2015 Plumbing and drainage – Sanitary plumbing and drainage;

The following guides, which are available at http://www.worksafe.govt.nz:

Excavation Safety – Good practice Guidelines,

Underground services – Guide for safety with underground services;

The following clauses, and any related compliance documents, which are available at https://www.building.govt.nz/:

New Zealand Building Code Clause E1 Surface Water;

New Zealand Building Code Clause G12 Water Supplies;

New Zealand Building Code Clause G13 Foul Water;

and all subsequent amendments and replacements.

2	Definitions

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturer instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

Trade waste – grease from food processing; petrol, oil, and lubricants (POL); laboratory waste; acid; high temperature liquids; or other waste as determined by relevant local authorities.

User – the person or persons who will discharge material into the trap, or their representative.

3	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of trade waste types, sources, and its interception for appropriate management.

Performance criteria

1.1	Describe key characteristics of types of trade waste that create the need for them to be intercepted for special handling.

1.2	Describe the sources of trade waste of different types.

1.3	Describe the appropriate responses when trade waste needs to be intercepted and managed.

Outcome 2

Demonstrate knowledge of the installation of trade waste interceptor traps.

Performance criteria

2.1	Describe the required features of trade waste interceptor traps.

2.2	Describe fittings and accessories that are commonly installed and connected to trade waste interceptor traps.

2.3	Describe safety and security requirements relating to the location of and access to trade waste interceptor traps.

Outcome 3

Demonstrate knowledge of good practice relating to the installation and hand-over of trade waste interceptor traps.

Performance criteria

3.1	Describe special precautions and work practices relating to the installation of trade waste interceptor traps, intended to avoid harm to people and damage to property, environment, other services, materials, tools, and equipment.

3.2	Describe the matters to be included in a hand-over briefing to the user.

Range	may include but is not limited to – safe operation, permitted types of discharge, permitted volumes of discharge, regular maintenance requirements, limitations on access.

| Replacement information | This unit standard and unit standard 30613 replaced unit standard 1102. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 26 October 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.