| Title | Demonstrate knowledge of installing and maintaining gas metering equipment, and interpretation of gas meter data |
| --- | --- |
| Level | 4 | Credits | 3 |

| Purpose | This unit standard is for people who work in the gasfitting industry. People credited with this unit standard are able to demonstrate knowledge of: – the installation, commissioning, and protection of gas metering equipment, in accordance with relevant legislation, regulations, codes, and standards; – the maintenance of gas metering systems; and – regulatory requirements, and underpinning concepts and principles, as applied to the installation, commissioning, and maintenance of gas metering equipment; and – how to interpret gas meter data. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Gasfitting |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Building Act 2004;

Gas Act 1992;

Gas (Safety and Measurement) Regulations 2010;

Health and Safety at Work Act 2015;

Plumbers, Gasfitters, and Drainlayers Act 2006;

Plumbers, Gasfitters, and Drainlayers Regulations 2010;

The following standards, which are available at http://www.standards.govt.nz:

AS/NZS 5601.1:2013 Gas installation,

NZS 5258:2003 Gas distribution networks,

NZS 3604:2011 Timber Framed Buildings,

NZS 5807:1980 Code of practice for industrial identification by colour, wording or other coding;

The following clause, and any related compliance documents, which are available at https://www.building.govt.nz/:

New Zealand Building Code Clause G11 Gas as an Energy Source;

and all subsequent amendments and replacements.

2	This unit standard applies to the installation, commissioning, and maintenance of subsidiary gas meters downstream of the point of supply as defined in the Gas (Safety and Measurement) Regulations 2010.

4	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

3	Definitions

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturer instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

Maintain may refer to all or any of – repair, upgrade, alter, remove, replace.

Gas metering systems (GMS) – a combination of the meter and any associated valves, filters, regulators, over pressure protection, and connections.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of the installation, commissioning, and protection of gas metering systems, in accordance with relevant legislation, regulations, codes, and standards.

Performance criteria

1.1	Describe the installation of gas metering systems.

1.2	Describe the connection of gas metering systems to connection and termination points.

1.3	Explain the testing, purging, and commissioning of gas metering systems.

1.4	Describe the requirements for protection of gas metering equipment.

1.5	Describe requirements to identify gas metering equipment by label and/or colour in accordance with relevant codes and standards.

Outcome 2

Demonstrate knowledge of the maintenance of gas metering systems.

Performance criteria

2.1	Explain the assessment of gas metering system to identify safe and proper operation and suitability for appliance demand in accordance with AS/NZS 5601:2013.

2.2	Describe how to identify faults in terms of causes and possible means of rectification.

2.3	Explain how to rectify faults in accordance with maintenance requirements and job specifications.

Range	must include but is not limited to – replacing meter, using meter bypass.

Outcome 3

Demonstrate knowledge of regulatory requirements, and underpinning concepts and principles, as applied to the installation, commissioning, and maintenance of gas metering equipment.

Performance criteria

3.1	Describe applicable sections of legislation, standards, and codes in terms of their application to the installation, testing, purging, commissioning, and maintenance of gas metering systems.

3.2	Explain underpinning concepts and principles in terms of their application to the reading and interpretation of gas meter data.

Range	correction factors, gas volumes, Charles’ law, Boyle’s law.

Outcome 4

Demonstrate knowledge of how to interpret gas meter data.

Performance criteria

4.1	Explain how to interpret gas meter data.

Range	before and after meter readings, applying correction factors for pressure, temperature.

| Replacement information | This unit standard replaced unit standard 2132. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 23 November 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.