| Title | Describe, receive, handle and store materials and products used in kitchen joinery work |
| --- | --- |
| Level | 4 | Credits | 8 |

| Purpose | People credited with this standard are able to describe, receive, handle and store materials and products used in kitchen joinery work. |
| --- | --- |

| Classification | Joinery > Joinery Operational Skills |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Legislation, standards, and guidelines relevant to this unit standard include:

- Building Act 2004;

- Construction Contracts Act 2002;

- Fair Trading Act 1986;

- Hazardous Substances and New Organisms Act 1996;

- Health and Safety at Work Act 2015;

- Heritage New Zealand Pouhere Taonga Act 2014;

- Resource Management Act 1991;

- Building Regulations 1992, available from www.legislation.govt.nz;

- AS/NZS 4386.1:1996 Domestic kitchen assemblies – kitchen units;

- NZS 3604:2011 Timber-framed buildings;

- NZS 4121:2001 Design for access and mobility: Buildings and associated facilities, available from www.standards.govt.nz;

- The Absolutely Essential Health and Safety Toolkit for Small Construction Sites, available from www.worksafe.govt.nz;

- New Zealand Certificate in Kitchen Joinery (Level 4) Specifications; September 2020; available from qualifications@waihangaararau.nz, and any subsequent amendments and replacements.

2	Assessment

Evidence for this unit standard must reflect commercial competence; the ability to demonstrate knowledge and skills in the context of the currently accepted requirements of a business operating in a commercial environment.

Evidence must also reflect commercial standards; the verbal and written information covering company policy, standard operating procedures and processes and job-specific instructions.

This unit standard must be assessed under the supervision of a commercially competent practitioner in workplace conditions that reflect:

- commercial standards, current health, safety, industry, and workplace requirements; and

- industry requirements for commercially acceptable timeframes.

3	Definitions

Kitchen joinery work refers to cabinetry that is fixed and may include bathroom, laundry, storage solutions, or wardrobe components.

Properties refer to those which require environmental consideration as well as compatibility with other materials and products.

Workplace requirements refer to the documented procedures specific to a workplace that which sets set out the standard and the required practices of that workplace.  This may include job specifications, procedures, practices, manufacturer recommendations, technical data sheets, material safety data sheets.

Outcomes and performance criteria

Outcome 1

Describe materials and products used for kitchen joinery work.

Performance criteria

  - Types of materials used in the manufacture and installation of kitchens are described in terms of their properties and use.

Range	materials include – timber, composite materials, laminates, veneers, and acrylics;

evidence of two from each type of material is required.

1.2	Types of hardware used in the manufacture and installation of kitchens are described in terms of their properties and use.

Range	hardware includes – handles, hinges, slides, adjustable plinth legs, catches, roller doors, rails, cutlery inserts, kitchen bins.

1.3	Types of fixings used in the manufacture and installation of kitchens are described in terms of their use.

Range	fixings include – screws, cams, biscuits, dowels, brads.

1.4	Types of adhesives and sealants used in the manufacture and installation of kitchens are described in terms of their properties and use.

Range	two adhesives and two sealants.

1.5	Types of benchtop inserts used in the manufacture and installation of kitchens are described in terms of their use.

Range	inserts include – bowls, sinks, drainers.

1.6	Kitchen appliances are described in terms of installation requirements.

Range	ventilation, clearance, position, shielding;

evidence of three appliance types is required.

Outcome 2

Receive, handle, and store, materials and products used for kitchen joinery work.

Performance criteria

2.1	Materials and products for kitchen joinery work are received, handled, and stored.

Range	materials, adhesives and sealants, hardware, mechanical fixings, inserts, appliances, electrical and plumbing items.

| Planned review date | 31 December 2028 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 June 2023 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0073 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Waihanga Ara Rau Construction and Infrastructure Workforce Development Council at qualifications@WaihangaAraRau.nz if you wish to suggest changes to the content of this unit standard.