| Title | Maintain aircraft in storage |
| --- | --- |
| Level | 4 | Credits | 6 |

| Purpose | People credited with this unit standard are able to: prepare to maintain aircraft in storage; and maintain aircraft in storage. |
| --- | --- |

| Classification | Aeronautical Engineering > Aircraft Mechanical Maintenance |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

- All tasks must be carried out in accordance with enterprise procedures.

- Definition

Enterprise procedures – procedures used by the organisation carrying out the work and applicable to the tasks being carried out.  Examples are – standard operating procedures, safety procedures, equipment operating procedures, codes of practice, quality management practices and standards, procedures to comply with legislative and local body requirements.

3	The scope of the systems that this standard relates to is described in the applicable chapters of ATA iSpec 2200.

Outcomes and performance criteria

Outcome 1

Prepare to maintain aircraft in storage.

Performance criteria

1.1	Task is determined by reviewing aircraft and/or servicing documentation.

1.2	Resources are obtained and checked for serviceability or status.

Range	may include but is not limited to – publications, tools, equipment, safety equipment, materials.

1.3	Aircraft to be maintained is identified by matching registration with servicing documentation.

Outcome 2

Maintain aircraft in storage.

Performance criteria

2.1	Aircraft is prepared for maintenance.

Range	doors and/or panels are opened and closed; blanks, locks, chocks and covers are removed, stowed and/or fitted; bonding leads and/or isolation tags are connected and disconnected.

2.2	Aircraft is inspected.

Range	airframe, power plant, landing gear; fuel contamination checks, system functional checks; foreign objects and bird nests removed; inhibitor and corrosion preventative restored.

2.3	Any defects are identified, located, and reported.

2.4	Defects are rectified.

2.5	Resources are checked for serviceability and returned to service or storage.

Range	tools, equipment, safety equipment.

2.6	Documentation is completed.

| Planned review date | 31 December 2024 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 19 June 1995 | 31 December 2016 |
| Revision | 2 | 7 August 1997 | 31 December 2016 |
| Revision | 3 | 8 May 2001 | 31 December 2016 |
| Review | 4 | 25 September 2006 | 31 December 2016 |
| Review | 5 | 18 June 2014 | 31 December 2021 |
| Review | 6 | 26 March 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0028 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact ServiceIQ qualifications@serviceiq.org.nz if you wish to suggest changes to the content of this unit standard.