| Title | Finish fibrous plaster |
| --- | --- |
| Level | 2 | Credits | 6 |

| Purpose | People credited with this unit standard are able to: stop and finish flat, and right angle corner, fibrous plaster areas; and clean up after work is completed. |
| --- | --- |

| Classification | Construction Trades > Fibrous Plaster |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Credit for this unit standard can be achieved on site through a registered assessor, or off site with an accredited training provider.

2	Definition

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications or recommendations; material specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; site or work specific requirements.

All work practices must comply with the following:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Building Act 2004;

AS/NZS 2589:2007 Gypsum linings – Application and finishing, available from Standards NZ (http://www.standards.co.nz);

Approved Code of Practice for the Safe Erection and Use of Scaffolding (Wellington: Occupational Safety and Health Service, Department of Labour, 1995) available at http://www.osh.govt.nz;

New Zealand Building Code.

Outcomes and performance criteria

Outcome 1

Stop and finish flat, and right angle corner, fibrous plaster areas.

Performance criteria

1.1	Level of finish required is identified from job specifications.

1.2	Access is arranged and complies with the Health and Safety in Employment Regulations 1995.

1.3	Stopping is applied by hand in accordance with manufacturer's recommendations.

1.4	Jointing reinforcing is applied in accordance with manufacturer's recommendations.

1.5	Joint finishing is applied to level of finish specified.

1.6	All operations are completed without damage to the workplace, tools, or plant.

Outcome 2

Clean up after work is completed.

Performance criteria

2.1	Tools and plant are maintained, cleaned, and stored in accordance with site practice.

2.2	Waste material is disposed of and workplace is cleaned in accordance with site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 20 April 2006 | 31 December 2024 |
| Revision | 6 | 25 January 2008 | 31 December 2024 |
| Review | 7 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.