| Title | Calibrate engineering measuring devices and equipment |
| --- | --- |
| Level | 4 | Credits | 4 |

| Purpose | People credited with this unit standard are able to demonstrate knowledge of the principles of calibration, and calibrate engineering measuring devices and equipment. |
| --- | --- |

| Classification | Mechanical Engineering > Engineering - Measurement |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

BS 870:2008, Specification for external micrometers.

BS 887:2008, Precision vernier callipers. Requirements and test methods.

BS 907:2008, Specification for dial gauges for linear measurement.

BS 939:2007, Engineers’ squares (including cylindrical and block squares. Specification.

BS 1643:2008, Specification for precision vernier height gauges.

BS 5204-1:1975, Specification for straightedges. Cast iron straightedges (bow shaped and I-section).

BS 5204-2:1977, Specification for straightedges. Steel or granite straightedges of rectangular section.

BS EN ISO 10012:2003, Measurement management systems. Requirements for measurement processes and measuring equipment.

2	Definition

Workplace procedures – procedures used by the organisation carrying out the work and applicable to the tasks being carried out.  Examples are – standard operating procedures, safety procedures, equipment operating procedures, codes of practice, quality management practices and standards, procedures to comply with legislative and local body requirements.

3	Recommended for entry

Unit 4439, Select, use, and care for complex engineering measuring equipment for precision jobs.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of the principles of calibration.

Range	examples of measuring devices and equipment are – squares, micrometers, vernier callipers, dial gauges, height gauges, straight edges, surface plate;

evidence is required for at least three different items of equipment.

Performance criteria

1.1	Purpose of instrument calibration is related to internationally accepted measurement standards such as those listed in the references.

1.2	Traceability chain is related to internationally accepted measurement standards such as those listed in the references.

1.3	Measurement uncertainty factors are explained relative to measurements obtained.

Range	standard, workpiece, instrument used for measurement, people, environment (SWIPE).

Outcome 2

Calibrate engineering measuring devices and equipment.

Performance criteria

2.1	Documents relevant to calibration are selected according to the task.

Range	includes but is not limited to – internationally accepted measurement standards such as those listed in the references, manufacturer's specifications, client specifications.

2.2	Calibration is carried out in accordance with internationally accepted measurement standards such as those listed in the references.

2.3	Measurement uncertainty is assessed and is applied to results.

2.4	Results are recorded according to workplace procedures, and compliance with internationally accepted measurement standards such as those listed in the references is confirmed.

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 23 May 1995 | 31 December 2011 |
| Revision | 2 | 14 April 1997 | 31 December 2011 |
| Revision | 3 | 5 January 1999 | 31 December 2011 |
| Revision | 4 | 23 May 2001 | 31 December 2011 |
| Review | 5 | 21 February 2005 | 31 December 2014 |
| Review | 6 | 17 June 2011 | 31 December 2022 |
| Review | 7 | 14 December 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0013 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Competenz qualifications@competenz.org.nz if you wish to suggest changes to the content of this unit standard.