| Title | Plaster floors, steps, and landings on site |
| --- | --- |
| Level | 4 | Credits | 23 |

| Purpose | People credited with this unit standard are able to: set up work area; apply plaster to prepared surfaces on site; and complete work operations. |
| --- | --- |

| Classification | Construction Trades > Solid Plastering |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

industry practice refers to the expected standard required in an on-site environment in which credit for this standard is sought; such standards may be set down in: industry codes of practice; documented procedures specific to standards endorsed by the BCITO - Solid Plastering and Floor and Wall Tiling Industry National Advisory Group; best practice descriptors; standards of practice which are regarded as desirable benchmarks for operations endorsed by the BCITO - Solid Plastering and Floor and Wall Tiling Industry National Advisory Group;

on site refers to a wide range of building and construction environments within which the trade skills must be applied;

site safety plan refers to the employer’s documented safety plan which demonstrates compliance with the Health and Safety in Employment Act, 1992.

2	The word plant is used as in the Health and Safety in Employment Act, 1992 to mean: appliances, equipment, fittings, furniture, implements, machines, machinery, tools, vehicles, plus parts, controls, and anything connected to such plant.

3	Specifications refers to any, or all of the following: manufacturer’s specifications and/or recommendations; site and/or work specific requirements.

4	All work practices must comply with the following Regulations, legislation and standards:

Health and Safety in Employment Act, 1992;

Health and Safety in Employment Amendment Act, 2002;

Health and Safety in Employment Regulations, 1995;

Resource Management Act, 1991;

Resource Management Amendment Act, 2003;

New Zealand Standard 4251: 1998, Code of Practice for Solid Plastering;

AS2592: 1983, Gypsum Plaster for Building Purposes.

Outcomes and performance criteria

Outcome 1

Set up work area.

Range	interior, exterior.

Performance criteria

1.1	Area to be plastered is in accordance with plan and specifications.

1.2	Actions taken in the event that surfaces are not in accordance with plan and specifications, are in accordance with industry practice.

1.3	Plant and materials are located in accordance with work flow.

Range	accessibility, services, protection against weather.

1.4	Work of other trades is protected prior to commencement of work.

1.5	Access equipment is erected to comply with regulations.

Outcome 2

Apply plaster to prepared surfaces on site.

Range	fall, levels.

Performance criteria

2.1	Site specific conditions affecting the application of plaster are determined and allowed for in accordance with industry practice.

2.2	Plaster is mixed in accordance with specifications.

  - Plaster is applied in accordance with plans and specifications and to take account of any site specific conditions.

  - Plastering finish is to the design requirements.

Range	steel trowel, sponge, wood float, broom finish.

Outcome 3

Complete work operations.

Performance criteria

3.1	All operations are completed without damage to project, plant, and materials.

3.2	All activities comply with the requirements set down in the site safety plan.

3.3	Workplace emergency procedures are followed as set down in the site safety plan.

3.4	All plant is used, maintained, cleaned, and stored in accordance with manufacturer’s and/or supervisor’s requirements.

3.5	Work site is left as specified in terms of contract with client.

3.6	Surplus materials are dealt with in accordance with industry practice, and to comply with legislation.

Range	non-hazardous, hazardous.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 28 June 1999 | 31 December 2024 |
| Review | 2 | 26 May 2004 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.