| Title | Install interior proprietary partitions under supervision |
| --- | --- |
| Level | 2 | Credits | 5 |

| Purpose | People credited with this unit standard are able to: prepare and set out for interior proprietary partitions under supervision; install interior proprietary partitions under supervision; and clean up after work is completed. |
| --- | --- |

| Classification | Construction Trades > Specialist Interiors |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refer to documented specifications and may include any of the following: drawings, project or job requirements, manufacturers’ specifications, recommendations or instructions, material specifications.

Work site practices refer to the practices generally acknowledged by the industry as being acceptable when no specific work site is relevant or available and refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

Plant is used as in the Health and Safety in Employment Act 1992 to mean: appliances, equipment, fittings, furniture, implements, machine, machinery, tools, vehicles, plus parts, controls, and anything connected to such plant.

2	Credit for this unit standard can be achieved on site through a registered assessor, or in a simulated environment with an accredited training provider.

3	All work practices must comply with the following:

Building Act 2004;

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

New Zealand Building Code.

Outcomes and performance criteria

Outcome 1

Prepare and set out for interior proprietary partitions under supervision.

Performance criteria

1.1	Type of partition is identified from manufacturer’s specifications.

1.2	Work site measurements are confirmed in accordance with work site practice.

1.3	Materials are accepted and stored to ensure specified quality is maintained in accordance with work site practice.

1.4	Positions of partitions are set out in accordance with working drawings and work site practice.

1.5	All operations are completed without damage to the work site, tools, or plant.

Outcome 2

Install interior proprietary partitions under supervision.

Range	plain, single door, single window.

Performance criteria

2.1	Partition framing is erected to line, level, and plumb.

2.2	Linings and panels are fixed in accordance with manufacturer’s specifications.

2.3	Partition details are completed in accordance with manufacturer’s specifications.

2.4	All operations are completed without damage to the work site, tools, or plant.

Outcome 3

Clean up after work is completed.

Performance criteria

3.1	Tools and plant are maintained, cleaned, and stored in accordance with work site practice.

3.2	Waste material is disposed of and work site is cleaned in accordance with work site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 19 May 2006 | 31 December 2024 |
| Revision | 6 | 25 January 2008 | 31 December 2024 |
| Review | 7 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.